Math skills/concepts required for

Automotive Service Technician

at Algonquin College.

- Very basic math skills (+), (-), (x), (÷).

- Area of a circle. Formula or area

- Circumference of a circle

- Volume of a cylinder; i.e. engine cylinder.

- Gear ratio calculation – formula

Ex:	Driven  X  Driven  = 30 X 38 = 1140 = 6.333 to 1

Drive         Drive     15     12     180

- Rounding decimals up or down.

Triangular formulas;

Hydraulic used in Brake System

F= Force  (in lbs)

P= PSI (pressure per sq.in.)

A= Area (sq. in.)

If  P = 100 psi & A = 2 sq in.   multiply  PxA = 200 lbs of force

If  F = 200 lbs & A = 2 sq in.   divide   F/A = 100 psi

Ohm’s Law

E = Voltage

I = Amperage

R = Resistance (ohms)

If  E = 12V and I = 6 amps    divide  R = 12/6 = 2 ohms (Ω)

If  I = 6 amps and R = 2 Ω     multiply  E = 6X2 = 12volts

Watt’s Law

P = Electrical Power – rated in Watts

I  = Amperage

E = Voltage

If  P = 100 watts and E = 120V  divide  I  = 100/120 = 0.8333 amps

If  I = 0.8333 amps and E = 120V  multiply  P = 0.8333 X 120 = 99.996 watts

(due to rounding)

- using fractions

+              -           x        ÷

- Formula for Total Circuit Resistance of a parallel Electrical Circuit.

1

__________________________

1    +    1    +    1    +    1

R1               R2             R3            R4				R1 = Resistance of leg 1

R2 = Resistance of leg 2

And so on…

= 		1					1				1

__________________________   =         ______________________    =     ___________

1     +    1    +    1    +    1		       6    +     4    +    12    +    3                      25

10         15         5          20		      60         60          60         60	           60

=     1    X     60  =    60   =   2.4 ohms

1            25         25